## Slide 1: MILP algorithms: branch-and-bound and branch-and-cut

## Slide 2: Content
The Branch-and-Bound (BB) method.
  the framework for almost all commercial software for solving mixed integer linear programs
Cutting-plane (CP) algorithms.
Branch-and-Cut (BC)
  The most efficient general-purpose algorithms for solving MILPs

## Slide 3: Basic idea of Branch-and-bound
BB is a divide and conquer approach: break problem into subproblems (sequence of LPs) that are easier to solve

## Slide 4: Decomposing the initial formulation P

## Slide 5: Enumeration tree
IP example 1:
How to proceed without
complete enumeration?
s
s
s

## Slide 6: Implicit enumeration: Utilize solution bounds

## Slide 7: Pruning (= beskjæring av tre)
Utilize convexity of the LP relaxations to prune the enumeration tree.
Pruning by optimality : A solution is integer feasible; the solution cannot be improved by further decomposing the formulation and adding bounds.
Pruning by bound: A solution in a node i is worse than the best known upper bound, i.e.
Pruning by infeasibility : A solution is (LP) infeasible.
Notes: Husk: konvekst problem, hvis integer feasible, kan ikke finne en bedre integer feasible løsning lengre ned i treet.
Husk: children node kan ikke være bedre enn foreldrenoden.

## Slide 8: Branching: choosing a fractional variable
Which variable to choose?
Branching rules
Most fractional variable: branch on variable with fractional part closest to 0.5.
Strong branching: tentative branch on each fractional variable (by a few iterations of the dual simplex) to check progress before actual branching is performed.
Pseudocost branching: keep track of success variables already branched on.
Branching priorities.

## Slide 9: Node selection
Each time a branch cannot be pruned, two new children-nodes are created.
Node selection rules concerns which node (and hence which LP) to solve next:
Depth-first search.
Breath-first search.
Best-bound search.
Combinations.

## Slide 10
L is a list of with the nodes
Initialize upper bound.
Assume LP is bounded
Solve and check LP relaxation
in root node
Select node a solve new LP
with added branching constraint
Check if solution can be pruned.
Removed nodes from L where the
solution is dominated by the best
lower bound
Choose branching variable,
add nodes to the list L of
unsolved nodes

## Slide 11: Earlier IP example
Branching rule: most fractional
Node selection rule: best-bound
s
s
s
s
s
s
s
IP:

## Slide 12: Software
Optimization modeling languages:
Matlab through YALMIP
GAMS: Generalized Algebraic Modeling System
AMPL: A mathematical programming language
MILP software:
CPLEX
Gurobi
Xpress-MP

## Slide 14: Recall the LP relaxation:
Notes: Check first: is y in conv(X)?
If not, find a cut.

## Slide 15: The Cutting-plane algorithm
s
Notes: The Cutting-plane algortihm er også omtalt som Gomorys CP algortime. Gomorys CP er kun et spesialtilfelle av den mer generelle CP, hvor algoritmen baserer seg på å bruke optimal basis av LP relaksering til iterativt å genere Chvatal-Gomory cutting planes (se side 124 og Th 8.4 side 120 i Wolsey IP bok.)

## Slide 16: Generating valid inequalities

## Slide 17: Example on cut generation: Chvátal-Gomory valid inequalities

## Slide 18: Branch-and-cut

## Slide 19: Earlier IP example: Branch-and-Cut
Branching rule: most fractional
Node selection rule: best-bound
s
s
s
IP:

## Slide 20: The GAP problem in GAMS with Branch and Cut

## Slide 21: Choice of LP algorithm in Branch and Bound
s
s
s
Very important for the numerical efficiency of branch-and-bound methods.
Re-use optimal basis from one node to the next.

## Slide 22: Solution of large-scale MILPs
Important aspects of the branch-and-cut algorithm:
Presolve routines
Parallelization of branch-and-bound tree
Efficiency of LP algorithm
Utilize structures in problem:
Decomposition algorithms
Apply heuristics to generate a
feasible solution

## Slide 23: MINLP: challenges

## Slide 24: MINLP: solution approaches
Source: ZIB Berlin

## Slide 25: Conclusions
Branch-and-bound defines the basis for all modern MILP codes.
Pure cutting-plane approaches are ineffective for large MILPs.
BB is very efficient when integrated with advanced cut-generation, leading to branch-and-cut methods.
Solving large-scale MINLPs are significantly more difficult than MILPs.